## Slide 1: Rigid Body Surface Impact
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Rigid Body Surface Collisions
When a rigid body impacts a surface, it has the potential to bounce off the surface just like a particle, but there is also the potential for rotation before or after impact, complicating the situation.

## Slide 3: Rigid Body Surface Collisions
With a rigid body surface collision, we will often be given a set of velocities before an impact and will need to solve for…
  The velocity of the center of mass of the body after impact.
    Usually in terms of normal and tangential components
  The angular velocity of the body after impact.
Three unknowns, means we will need three equations to work with.

## Slide 4: Rigid Body Surface Collisions
In order to generate three equations, we will need to rely on the normal and tangential directions, just as we did with particle surface collisions.
  The tangential direction is parallel to the surface
  The normal direction is perpendicular to the surface
We will also look specifically at two points
  The center of mass of the body (G)
  The point of impact (P)
t
n
Fimpact
G
P

## Slide 5: Rigid Body Surface Collisions
t
n
Fimpact
G
P
Assuming that there is no friction force during impact, there is no force at all to change the velocity of the body in the tangential direction.
This applies specifically to the center of mass of the body

## Slide 6: Rigid Body Surface Collisions
t
n
Fimpact
G
P
Next, the coefficient of restitution can be applied to the body.
This is the normal velocity at the point of impact on the body.

## Slide 7: Rigid Body Surface Collisions
t
n
Fimpact
G
P
Finally, as there are no moments at the point of impact, the angular momentum of the body will be conserved about the point of impact.
Since the point of impact is generally not the center of mass or an instant center, we will need to use the angular momentum about any point relationship as follows.

## Slide 8: Rigid Body Surface Collisions
Putting this all together, we have three equations that should allow us to solve for up to three unknowns.
We can see this includes some velocities at the center of mass (G) and some velocities at the point of impact (P)
Because of this, the equations will usually need to be supplemented with kinematic relationships, in this case relating the velocity of the point of impact to the velocity of the center of mass and angular velocity.

## Slide 9: Solving Rigid Body Surface Impact Problems
Start by creating a diagram showing the initial and final states.
  Identify any known and unknown values.
  Identify the normal and tangential directions.
  Identify the point of impact (P) and the center of mass (G) of your body.
Next, write out the equations discussed in the slides and enter in known values.
  Add an equation relating motion at P to motion at G if necessary.
Solve your equations for the unknown values.

## Slide 10: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 11: Worked Example
An 80 centimeter long 1 kilogram metal bar falling at 2 meters per second strikes the edge of a table as shown below. Assuming a coefficient of restitution of .9, what is the expected velocity and angular velocity of the bar after impact?

## Slide 12: Worked Example
The square crate (dimensions a x a = 0.8 m x 0.8 m, mass m = 20 kg) has an initial angular velocity just before impact of ω1 = 4 rad/s. It impacts the ground at corner B (perfectly plastic impact). Determine the angle, θ, through which the crate will rotate upwards and the percentage of energy lost in the impact. Assume friction prevents slipping throughout.

## Slide 13: Worked Example
The rod AB (length L = 2 m, mass 15 kg) falls from rest from an initial angle of θ = 30 degrees. It impacts the corner C (b = 1.3 m). Determine the angular velocity, ω, and the velocity of the rod’s center of gravity, vG, just after impact.