## Slide 1: Internal Forces
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Internal vs. External Forces
Up until this point in statics we have been talking about external forces.
  These are any forces exerted on one body by some other body.
Whenever external forces are exerted on a body however, internal forces and internal moments must exist within the body to balance out these external forces.

## Slide 3: Internal Forces
a
a
a
a

## Slide 4: Internal Forces
At any one cross section we will have up to two types of internal forces and two types of internal moments.
  Normal forces exist perpendicular to your cross-section.
  Shear forces exist parallel to your cross section.
N
V2
V1

## Slide 5: Internal Moments
At any one cross section we will have up to two types of internal forces and two types of internal moments.
  Torsional Moments exist perpendicular to your cross-section.
  Bending Moments exist parallel to your cross section.
T
M2
M1

## Slide 6: Determining Internal Forces
To find the internal forces and internal moments, we can either…
  Imagine cutting the body at the cross section and performing an equilibrium analysis of one half of the body.
    This is similar to the method of sections
  We can use a graphical method to determine the normal forces, shearing forces, torsional moments, or bending moments across range of cross sections.

## Slide 7: Thanks for Watching
See other engineering mechanics videos and access the full tool at…