## Slide 1: Particle Collisions in One Dimension
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Collisions and Impulse
One instance in which the impulse momentum equations are particularly useful is when we have bodies colliding.
If a collision between two bodies occurs quickly…
  We will have a system of particles, and we will analyze the system as a whole with one impulse momentum equation
  The internal impulses exerted between the bodies colliding will cancel each other out (because of Newton’s Third Law)
  External impulses will generally be negligible because of the short time frame (they will be dwarfed by the magnitude of the internal forces of the collision)

## Slide 3: The Conservation of Momentum
Assuming we have no significant external impulse on the bodies colliding, we will have no change in momentum.
In this way the momentum is conserved.
Breaking the momentum down by body (Body A and Body B) and by pre and post collision status, we arrive at the following equation, our conservation of momentum equation
A
B

## Slide 4: Supplementing Our Conservation of Momentum Equation
With one equation (the conservation of momentum equation) we will be able to solve for one unknown.
Since this usually isn’t enough, we will need to get a second equation so we can solve for a second unknown (usually the final velocities of each particle).
The second equation we use will depend upon the type of collision
  Conservation of momentum is always the first equation, regardless of collision type.

## Slide 5: Types of Collisions
Elastic collisions:
  Usually a good approximation of two rigid bodies colliding without permanent deformation.
  100% of the kinetic energy is conserved.
Semi-Elastic collisions:
  Somewhere between elastic and inelastic.
  More kinetic energy conserved than in inelastic collision, less than 100% of kinetic energy conserved though.
  Coefficient of restitution relates kinetic energy before to kinetic energy after.
Inelastic collisions
  Occurs when bodies stick together after colliding.
  Velocities of two bodies are the same after collision.
  Lowest amount of kinetic energy conserved (still some is conserved)
Perfect Bounce
No Bounce
Some Bounce

## Slide 6: Elastic Collisions
In an elastic collision we have two conservation equations that will guide our analysis.
First, the conservation of momentum...
  Which can be broken down into x, y and z components.
And second, the conservation of kinetic energy...
  Which cannot be broken down into components (energy has no direction)

## Slide 7: Inelastic Collisions
In inelastic collisions we again have two sets of equations to that will guide our analysis.
The first is again the conservation of momentum...
  Which can be broken down into x, y and z components.
The second equation states that the final velocities of the bodies must be identical, because the bodies stick together in an inelastic collision.

## Slide 8: Semi-Elastic Collisions
In semi-elastic collisions we will again have two sets of equations, but we will also have another unknown, the coefficient of restitution which is a measure of the kinetic energy loss.
Again the conservation of momentum applies...
  Which can be broken down into x, y and z components.
The second equation we can use if the definition of the coefficient of restitution.

## Slide 9: The Coefficient of Restitution
For a simple body bouncing off a rigid surface such as the basketball to the right, the coefficient of restitution is the ratio of the velocity after the bounce to the velocity before the bounce.
If we have two bodies that can both have a velocity, it is the relative motion between the two bodies.

## Slide 10: Solving a Collision Problem (The Process)
Solving collision involves three steps, carefully accounting for the factors at play between some initial state and some final state.
Set up one diagram showing the initial state and set up some other diagram for the final state.
  Identify the known or unknown velocities in each state
  Identify the type of collision, and the coefficient of restitution if applicable
Use the diagram to put together the conservation of momentum equation along with the other appropriate equation for the collision type, with included known and unknown values.
  Conservation of energy, same final velocity, or coefficient of restitution equation
Solve the equations for the unknown quantities

## Slide 11: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 12: Worked Example
A cue ball weighing .17kg is traveling 1 m/s impacts a stationary billiard ball with a mass of .15kg as shown below. If the balls collide directly and the collision is elastic, what will the velocities be after the collision (ignore rotational energies)?
1 m/s

## Slide 13: Worked Example
A 4.2g bullet traveling at 965 m/s becomes lodged in a stationary log with a mass of 1.5kg. Assuming an inelastic collision...
  determine the velocity of the log and the bullet after the collision.
  Determine the percentage of the kinetic energy that is lost in the collision.
965 m/s

## Slide 14: Worked Example
Two masses on a frictionless rod as shown below are set to impact with each other. If the coefficient of restitution between the objects is .6...
  What is the velocity of each body after the collision?
  The percentage of the kinetic energy that is lost in the collision?
A
2kg
B
.75kg
3 m/s
1 m/s