## Slide 1: Dry Friction
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Friction
Friction is the force that prevents objects from sliding relative to one another.
  Sometimes this force is useful (as in the brakes on a car)
  Sometimes this force is not useful (as in the drag force that slows a plane down)
It is generally broken down into two types of friction.
  Dry friction (also called Coulomb Friction) is the friction between two solid objects sliding against one another.
  Fluid friction is the friction exerted by fluids on solid objects or other fluids flowing through them.

## Slide 3: The Nature of the Dry Friction Force
Force Pushing on Book (Fpush)
Friction Force Pushing Back
(Ffriction)
A perfectly rough surface
A real surface

## Slide 4: Static and Kinetic Friction
Force Pushing on Book (Fpush)
Friction Force Pushing Back
(Ffriction)
Until the point where…
After that point the friction force often drops down to and stays at…
no relative motion
relative motion
impending motion

## Slide 5: Variables in the Friction Equations
The friction coefficients. Depends on the materials in contact with one another.
The normal force between the two surfaces. The force pressing the two forces together.

## Slide 6: Friction Forces
As a review,
  Before an object reaches the point of impending motion, the friction force is whatever is necessary to keep the body from moving.
  At the point of impending motion
  Once the body starts sliding
Also remember that the friction force is based on the normal force, not the weight force of an object.

## Slide 7: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 8: Friction Worked Example
A 500 lb box is sitting on concrete floor. If the static coefficient of friction is .7 and the kinetic coefficient of friction is .6:
  What is the friction force if the pulling force is 150 lbs?
  What pulling force would be required to get the box moving?
  What is the minimum force required to keep the box moving once it has started moving?

## Slide 9: Friction Practice Problem
A 30 lb sled is being pulled up an icy incline of 25 degrees. If the static coefficient of friction between the ice and the sled is .4 and the kinetic coefficient of friction is .3, what is the required pulling force needed to keep the sled moving at a constant rate?

## Slide 10: Friction Worked Example
A plastic box is sitting on a steel beam. One end of the steel beam is slowly raised, increasing the angle of the surface until the box begins to slip. If the box begins to slip when the beam is at an angle of 41 degrees, what is the static coefficient of friction between the steel beam and the plastic box?