## Slide 1: Area Moments of Inertia via The Method of Composite Parts
Dr. Jacob Moore
Associate Professor of Mechanical Engineering
Penn State Mont Alto

## Slide 2: Finding Moments of Inertia for Composite Areas or Bodies
As an alternative to using integration to find area or mass moments of inertia, we can use lookup tables along with the parallel axis theorem to find a combined moment of inertia for a composite body.
In this way, we can skip the integration, instead using the work of others as a shortcut.
This is similar to the method we used to find the centroid or center of mass of a composite body.

## Slide 3: Finding Moments of Inertia for Composite Bodies or Areas
The overall process is as follows
Break the composite shape down into simple shapes that are in the lookup tables.
Look up the moments of inertia for each individual shape using the moment of inertia tables.
Use the parallel axis theorem to adjust moments of inertia to the common origin point.
Add the adjusted moments of inertia together to find the overall moment of inertia for the combined shape.

## Slide 4: Method of Composite Parts
The first step in finding the combined moment of inertia, is to break our complex shape into simple shapes that are in our moment of inertia tables.
  Holes or cutouts can be negative areas
  It is also useful to identify axes, and an origin point at this point to use in calculations
1 .
2
3
X
Y

## Slide 5: Method of Composite Parts
Next you are going to create a table to keep track of the various values.
  Each row will be used for one part
  The columns will vary from problem to problem but generally follow the format below.
1 .
2
3
Shape | Area |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
Total |  |  |  |  |  |  |  |  | 
Shape | Area |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
Total |  |  |  |  |  |  |  |  | 
X
Y

## Slide 6: Method of Composite Parts
After determining the area or mass of each piece, the next step is to find the centroid location of each piece as well as the overall centroid location.
  We will generally be taking the moment of inertia for the composite body about this overall centroid location.
  Even if you are given the overall centroid location, we will still need to know the centroid location for the individual pieces.

## Slide 7: Method of Composite Parts
Next, you will look up and calculate the moments of inertia about their individual centroids.
  Be sure to adjust the orientation to match the table to your situation .
1 .
2
3
X
Y

## Slide 8: The Parallel Axis Theorem
The parallel axis theorem states that...
Area Moment about any Point P
Area Moment about the Centroid
Area of Shape
Distance between the two x axes

## Slide 9: The Parallel Axis Theorem
The r value represents the distance you need to move the axis to “adjust” it to the new centroid or center of mass.
We are going to use the earlier centroid values in the table to find this adjustment distance “r”
1 .
2
3

## Slide 10: The Parallel Axis Theorem
It’s important to determine how far the axis has moved, not necessarily how far the centroid has moved.
Regardless of direction, we can count the distance as positive.
x
y
x
y
C
P

## Slide 11: Method of Composite Parts
Once you have figured out your r values, you will use those to find the adjusted moments of inertia for each piece.
Finally, the adjusted moments of inertia can be added up find the overall moment of inertia.
Shape | Area |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
Total |  |  |  |  |  |  |  |  | 
Shape | Area |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
Total |  |  |  |  |  |  |  |  | 

## Slide 12: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 13: Area Moment of Inertia Worked Example
A beam is made by connecting two 2 in by 4 in beams in a T pattern with the cross section as shown below. Determine the location of the centroid of this combined cross section and then find the rectangular area moment of inertia about the x axis through the centroid point.
2 in
4 in
4 in
2 in