## Slide 1: Kinetics in Belt and Gear Driven Systems
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Newton’s Second Law and Kinetics
In kinetics, we can build directly on Newton’s second law which states that...
In rigid body kinetics, we can additionally apply the rotational version of Newton’s second law…
If we put known forces, moments, masses, mass moments of inertia and accelerations into these equations for a given system, we have the equations of motion for that object.
By solving these equations, we can find either the forces or moments given the accelerations, or the accelerations given the forces and moments.

## Slide 3: Fixed Axis Rotation and the Mass Moment of Inertia
Despite its simplicity, fixed axis rotation very common in engineered systems.
Within the moment equation () the new term is the mass moment of inertia, where the mass moment of inertia represents an objects resistance to rotation about a given axis.
Details on how to calculate the mass moment of inertia are in Appendix 2

## Slide 4: Balanced Fixed Axis Rotation Systems
In instances where a body is rotating about some fixed axis at its center of mass, we will have moments and angular accelerations at play while the sum of the forces will be equal to zero.
In instances of balanced fixed axis rotation, we can sum the moments about the fixed axis of rotation (which is also the center of mass).
  Make sure both the moments and the mass moment of inertia are taken about this point.

## Slide 5: Unbalanced Fixed Axis Rotation Systems
In instances where a body is rotating about some fixed axis that is not it’s center of mass, we will have forces and moments at play.
  or
In instances of unbalanced fixed axis rotation, we can sum the moments about the fixed axis of rotation or about the center of mass.
  Just make sure you are consistent

## Slide 6: Solving a Rigid Body Kinetics Problem (The Process)
The process used in solving a kinetics problem is similar to solving a problem in statics and consists of three steps.
Set up a free body diagram.
  Draw the body separated from it’s surroundings
  Draw in all the known and unknown forces (I use red for forces) as well as key dimensions and angles (I use blue for dimensions and angles)
  Draw in the acceleration vectors (I use a blue dashed vector for this)
Use the free body diagram to write out your equations of motion, breaking all forces down into x and y components, and writing out all the moments about the center of mass of the body or the fixed axis of rotation.
  These may be supplemented with kinematics equations.
Solve the equations for any unknowns.

## Slide 7: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 8: Worked Example
If a torque of 60 Nm is applied to the input pulley A, what is the expected torque at the output pulley D? Assume the mass of the pulleys is negligible.

## Slide 9: Worked Example
In the following gear train, gear A is in contact with gear B. Gear B and gear C are rigidly attached, and gear C is in contact with gear D. If we wish to have an output torque of 5kNm at gear D, what is required input torque at A? Assume the gears have negligible mass and that rA=1m, rB=3m, rC=0.5m, and rD=1.5m.

## Slide 10: Worked Problem
The drum in a washing machine can be approximated as a cylinder with a diameter of 80 cm, a depth of 60 cm, and a mass of 30 kg. The drum is driven by a belt that connects the outside of the drum to a 10 cm diameter pulley, which is driven by a motor. If we wish for the drum to accelerate at a rate of 5 rad/s2, what torque should the motor apply to the input pulley? Assume the pulley itself has negligible mass?
drum
in