## Slide 1: The Equivalent Point Load
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: The Equivalent Point Load
The equivalent point load is a single point force that is statically equivalent to some original distributed force.
  It would cause the same acceleration and angular acceleration as the original distributed force
  It would cause the same reaction forces as the original distributed force

## Slide 3: Why Use The Equivalent Point Load
Distributed forces are difficult to deal with directly in the equilibrium equations.
  We would have integrals in our force and moment equations
Because of this, we usually convert the distributed force into it’s equivalent point load before proceeding with static or dynamic analysis.

## Slide 4: Finding the Equivalent Point Load
For any point force we must define...
  The magnitude
  The direction
  The point of application
For now we will only deal with distributed loads with a uniform direction, so the direction will just be maintained.

## Slide 5: Finding the Equivalent Point Load
To determine the following...
  The magnitude
  The point of application
We have two options.
  Calculation via Integration
  Calculation via Composite Parts

## Slide 6: Statically Equivalent Systems (A lead-in to the Equivalent Point Load)
Imagine we have a cantilever beam with a few forces acting on the beam.
How might we find the magnitude and location of a single force that is statically equivalent to the original set of forces
60 N
30 N
50 N
5 m
2 m
3 m

## Slide 7: The Equivalent Point Load via Integration
We can imagine a distributed force as an infinite number of very small forces.
Rather than summing all of these forces as we did before to find the magnitude of the equivalent point load, we will take the integral to find the area under the force function.

## Slide 8: The Equivalent Point Load via Integration
An important first step is to define the force function “F(x)”.
  In a 1-D problem like this, the force function will give you the magnitude of the distributed force (in units of force per given length) at any given value of x.
F(x) is the equation describing this curve at any given value of x

## Slide 9: The Equivalent Point Load via Integration
Next we will determine the point of application of the equivalent point load (xeq), by knowing that the moment exerted by the original distributed force must be equal to the moment exerted by the equivalent point load.
To find the moment exerted by the distributed force, we use the moment integral, integrating the equation that is the force function times the distance (x).

## Slide 10: The Equivalent Point Load via Integration
By rearranging the equation from the previous slide, we can solve directly for the location of the force (xeq).

## Slide 11: Discontinuous Force Functions
Occasionally we will come across a force function (F(x)) that cannot be written out as a single continuous function.
In cases like this we will split the function into sections, integrate each section in it’s given range, and add together the results.

## Slide 12: Discontinuous Force Functions
To find the magnitude of the equivalent point load, find the equation describing the magnitude of the force function for each section, then integrate each section within it’s respective range, then add together the two integrals.
x1
x2
x3

## Slide 13: Discontinuous Force Functions
To find the location of the equivalent point load we can go through a similar procedure with the moment integrals.
x1
x2
x3

## Slide 14: The Equivalent Point Load for 2-D Surface Forces
Now we will look at a force spread over two dimensions (x and y).
Again the first step is to define the force function.
  This will a function describing the pressure at a given x and y value.

## Slide 15: The Equivalent Point Load in 2-D Surface Force Problems
The volume under the force function is the magnitude of the equivalent point load.
We need to integrate the force function over the area the force is applied to in order to find this volume.

## Slide 16: The Equivalent Point Load in 2-D Surface Force Problems
To find the point of application of the equivalent point load, we now need two numbers (the x and y coordinates).
We multiply the force function by x for the x coordinate and the force function by y for the y coordinate.

## Slide 17: The Equivalent Point Load in Body Force Problems
We can go one step further in body force problems, integrating the force function over the volume of the distributed force.
And finding all three coordinates for the point of application.

## Slide 18: The Equivalent Point Load via Composite Parts
As an alternative to using integrals, we can also use the method of composite parts to find the magnitude and position of the equivalent point load.
  This will be a geometry-based solution, rather than calculus-based solution.

## Slide 19: The Equivalent Point Load via Composite Parts
As we stated before, the magnitude of the equivalent point load will be the area under the force function.
The position can be determined by knowing that the equivalent point load will travel through the centroid of the shape under the force function.

## Slide 20: The Equivalent Point Load via Composite Parts for Surface Forces
We can use a similar approach for surface forces
  The magnitude of the equivalent point load will be the volume under the force function.
  The equivalent point load will travel through the center of volume (same as center of mass for a uniform density object).

## Slide 21: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 22: Equivalent Point Load via Integration Worked Example
Determine the magnitude and location of the equivalent point load for the distributed force shown below using composite parts.
3 m
7 m
14 kN/m

## Slide 23: Equivalent Point Load via Integration Worked Example
Determine the magnitude and location of the equivalent point load for the parabolic distributed force shown below. (assume a slope of zero at the wall)
1800 lbs/ft
3 ft

## Slide 24: Equivalent Point Load via Integration Worked Example
Determine the magnitude and location of the equivalent point load for the distributed force shown below using integration.
5 m
5 m
10 kN/m

## Slide 25: Equivalent Point Load via Integration Worked Example
Determine the magnitude and location of the equivalent point load, then use that to find the magnitude of the reaction forces at A and B.
6 kN/m
6 m
4 kN/m
A
B
6 m

## Slide 26: Equivalent Point Load via Integration Worked Example
An empty truck trailer with a weight of 17000 lbs is subjected to the wind force shown to the right. Assuming the weight acts in the middle of the trailer, what is the expected normal forces at the tires on the left and the tires on the right?
700 lbs/ft
400 lbs/ft
9 ft
2 ft
8 ft
A
B