## Slide 1: Varignon's Theorem
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Varignon’s Theorem
Varignon’s Theorem, often called the principle of moments, states that…
“If we have two or more concurrent forces, the sum of the moments that each force creates about a single point will be equal to the moment created by the sum of those forces about the same point.”

## Slide 3: Varignon’s Theorem
In the case below, F1 + F2 = Ftotal, and we are taking the moment about point A.
We have two alternate paths to find the overall moment about point A.
  Add F1 and F2 to find Ftotal, then find the moment Ftotal exerts about point A.
  Find the moment from F1, the moment from F2, and add those two moments together.

## Slide 4: Varignon’s Theorem in Reverse
Varignon’s Theorem is more commonly used in reverse, breaking a single vector into components then finding the moment exerted by each component.
dx
F
M
M = Mx + My = (Fx * dy) + (Fy * dx)
My
Mx
dy
Fy
Fx

## Slide 5: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 6: Varignon's Theorem Worked Example
Use Varignon's Theorem to find the moment that the forces in the diagram below exert about point A.

## Slide 7: Varignon's Theorem Worked Example
Use Varignon's Theorem to determine the moment that the force at point A exerts about point B.

## Slide 8: Varignon's Theorem Worked Example
Use Varignon's Theorem to determine the moment that the force shown below exerts about the base of the post at point O.
2m
65o
6kN
20o
O