## Slide 1: Principle of Transmissibility
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Principle of Transmissibility
The principle of transmissibility states that the point of application of a force can be moved anywhere along its line of action without changing the impact of the force on the body.

## Slide 3: Principle of Transmissibility
As an example, a person pushing a cart with a 100-pound force will cause the same result as a person pulling the cart with a 100-pound force.
100 lbs
100 lbs

## Slide 4: Principle of Transmissibility
When forces of the same magnitude and direction do not share the same line of action, they will always produce dissimilar results, and they are not interchangeable.
100 lbs
100 lbs
100 lbs

## Slide 5: Principle of Transmissibility
An important note with the principle of transmissibility, is that it is only relevant for external forces and net accelerations.
If we are looking at internal forces or stresses, then the principle of transmissibility should not be applied.

## Slide 6: Thanks for Watching
See other engineering mechanics videos and access the full tool at…