## Slide 1: Equilibrium Analysis in Concurrent Force Systems
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Equilibrium Analysis
In equilibrium analysis, we are examining a body that is in equilibrium, using the forces and geometry we know, to solve for unknown forces or other unknown values.
45o
30o
F1 = 600 lbs
F2 = ?
F3 = ?
X
Y

## Slide 3: Equilibrium Analysis
To determine these unknown forces, we use the process of equilibrium analysis, which consists of the following steps:
  Draw a free body diagram of the body in the problem, showing all known and unknown forces.
  Use the free body diagrams to write out the equilibrium equations
  Solve the equilibrium equation for the unknowns.

## Slide 4: Creating a Free Body Diagrams
Draw a picture of the body being analyzed separate from all the background objects.
Draw in any forces acting on the body.
  Normal forces at any point of contact
  Gravitational forces
  Friction forces on rough surfaces
  Tension in any cables or wire.
  etc.
Add any angles for the force vectors and any key dimensions

## Slide 5: Creating a Free Body Diagrams
1 m
1 m
2 m
65o
Problem Diagram
Free Body Diagram

## Slide 6: Equilibrium Equations
For a body in equilibrium, we then know that...
To solve this vector equation, we break down the vectors into components, and write out the component equations...
and...
This gives us scalar equations, which we can solve with simple algebra.
  It also happens to turn our one equation into two equations (or three equations in 3D).
x and y components of the vectors

## Slide 7: Solving the Equilibrium Equations
In a simple concurrent force system in two dimensions, we will have two equations.
This means we can solve for up to two unknown values.
In a simple concurrent force system in three dimensions, we will have three equations.
This means we can solve for up to three unknown values.

## Slide 8: Moments and Concurrent Force Systems
For now we are only working with concurrent force systems, and we are only working with force equilibrium equations.
When we work with non-concurrent force systems, we will need to additionally need to sum the moments to be equal to zero.
  This will make problems more complex, but also give us more equations to solve for more unknowns.
concurrent
non-concurrent

## Slide 9: Equilibrium Analysis (Review)
To determine these unknown forces, we use the process of equilibrium analysis, which consists of the following steps:
  Draw a free body diagram of the body in the problem, showing all known and unknown forces.
  Use the free body diagrams to write out the equilibrium equations
  Solve the equilibrium equation for the unknowns.

## Slide 10: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 11: Concurrent Equilibrium Analysis Worked Example
Find the magnitudes of the normal forces acting on this barrel.
45o
30o
F1 = 600 lbs
F2 = ?
F3 = ?
X
Y

## Slide 12: Concurrent Equilibrium Analysis Worked Example
The 6 kg traffic light shown below is supported by two cables. Find the tension force in the two cables.
X
Y

## Slide 13: Concurrent Equilibrium Analysis Practice Problem
A flexible cable supports this mass as shown below. Determine the tension in the cable and the normal force acting on the mass.
400 kg
45o
15o

## Slide 14: Particle Equilibrium Worked Example
Two barrels are being carried on a handcart as shown below. Determine the forces acting on the bottom barrel.
B
200 lbs
A
150 lbs
30o

## Slide 15: Particle Equilibrium Practice Problem
Three soda cans, each weighing .75 lbs and having a dimeter of 4 inches, are stacked in a formation as shown below. Assuming no friction forces, determine the normal forces acting on can B.
A
B
C
9 in

## Slide 16: Particle Equilibrium in 3D Worked Example
The SkyCam at a sporting event has a mass of 20 kg and is supported by three cables as shown below. Determine the tension in each of the cables.

## Slide 17: Particle Equilibrium in 3D Worked Example
A hot air balloon is tethered to the ground with three cables as shown below. Determine the tension in each of the three cables.