## Slide 1: Couples
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Couples
A couple is a set of equal and opposite, but not collinear forces.
This pair of forces exerts no net force on the body, though it will exert a moment.
A
B
1 ft
1 ft
2 ft

## Slide 3: Couples
Because couples exert no net force on the body, they are also sometimes called pure moments
  These couples can either be represented as a set of forces, or simply as the moment these forces exert.

## Slide 4: Couples
In addition to exerting no net force, couples also have another interesting characteristic, they will exert the same moment about every point.
A
B
1 ft
1 ft
2 ft

## Slide 5: The Moment of a Couple
Where:
  M is the moment exerted by the couple at any point.
  F is the magnitude of each force.
  d is the perpendicular distance between the two lines of action of the force vectors.
A
B
d

## Slide 6: Couples
One other thing to look out for is the distance between the force vectors.
This is the minimum (perpendicular) distance between the lines of action of the forces.
1.5 m
45o
d

## Slide 7: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 8: Couple Worked Example
Find the moment exerted by the couple shown in the diagram below.

## Slide 9: Couples Practice Problem
Find the moment that the couple in the diagram below exerts.