## Slide 1: Moment of a Force About an Axis (vector calculation)
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: Moment of a Force About an Axis
Occasionally, we want to find the moment that a force exerts about a specific axis.
For example, the force shown in the diagram below will exert a moment about the bottom hinge (a point)
  Some part of that moment will be about the axis of the hinges (the y axis)
  Some part of that moment will be about other axes.

## Slide 3: Moment of a Force About an Axis
We will want to find the component of the moment vector about a point that lines up with the axis we are interested in.
We can use the dot product to do this.

## Slide 4: Moment of a Force About an Axis
The force vector
A vector going from any point on the axis we are taking the moment about to any point on the line of action of the force
A unit vector along the axis we are taking the moment about

## Slide 5: The Dot Product
Like the cross product, the dot product can be calculated by hand or calculated with computer tools.
Unlike the cross product, the dot product results in a single scalar value.
  This value represents the magnitude of the moment about the given axis.
  The moment direction is specified by the vector u.

## Slide 6: The Dot Product
The dot product can be calculated using the following strategy.
  First find the moment about a point ()
  If the u vector points along one of the three coordinate axes (x, y, or z) then the dot product will simply be that component of the original moment vector ()

## Slide 7: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 8: Moment About an Axis Worked Example
An L shaped plate lies in the XY plane and is supported by hinges at one end. Determine the moment that the force exerts about the axis of the hinges.