## Slide 1: Structures
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: What is a Structure?
A structure is any collection of connected bodies

## Slide 3: Types of Structures
Truss – Rigid assembly made entirely of two-force members.
Frame – Rigid assembly containing at least one member that is not a two-force member.
Machine – Non-rigid assembly containing at least one member that is not a two-force member.

## Slide 4: Analyzing Structures
As with everything in statics, the structure is assumed to be in equilibrium.
Because the structure is in equilibrium, each member (part of the structure) is also in equilibrium.
We analyze structures by breaking them down into parts and then performing static analysis on the pieces.

## Slide 5: Important Factors for Structure Analysis
When making the jump from analyzing a single body to analyzing a collection of bodies, the two most important factors are...
The application of Newton’s Third Law.
The identification of Two Force Members.

## Slide 6: Newton’s Third Law
Newton’s Third states that “for every action (force) there is an equal and opposite reaction (other force)”.
In a structure, this means that whenever two bodies are connected, the force that body A exerts on body B will be equal and opposite to the force that body B exerts on Body A.

## Slide 7: Newton’s Third Law
Though you analyze each body separately, Third Law pairs of forces will exist wherever two separate members in the structure are connected to one another.
These pairs will be equal in magnitude but opposite in direction.
This reduces the number of unknowns you will need to solve for.

## Slide 8: Two Force Members
The next important factor is to look for two-force members.
A two-force member is a body that has forces (and no moments) exerted at only two points.

## Slide 9: Two Force Members
A two-force member will have two equal, opposite, and collinear forces acting on it.
  This is a result of Newton’s Second Law
This will also reduce the number of unknowns you will need to solve for.

## Slide 10: Methods for Analyzing Structures
Identify the type of Structure you have
  Trusses
    Method of Joints
    Method of Sections
    Hybrid of Joints and Sections
  Frames and Machines
    Analysis of Frames and Machines
      Relies heavily on Newton’s Third Law
      Still important to identify two force members

## Slide 11: Thanks for Watching
See other engineering mechanics videos and access the full tool at…