## Slide 1: Shear and Moment Diagrams
Dr. Jacob Moore
Associate Professor of Engineering
Penn State Mont Alto

## Slide 2: The Graphical Approach
By splitting a body at a specific point and performing an equilibrium analysis, we can find the internal forces and moments at that point.
  If we want to look at a second point, we will need a second analysis.
Often however, it will not be obvious where those internal forces or moments will be the highest, and we may want to look at several possible points.
A graphical approach can be used to plot the normal forces, shearing forces, torsional moments, or bending moments along the axis of the body, allowing us to easily pick out the maximum values.

## Slide 3: Shear and Moment Diagrams
In a beam, we can use some simple rules to plot out the internal shearing forces in that beam.
We can then use the shear diagram and some additional information to plot out the internal bending moments in the beam.
Both plots are frequently used to examine horizontal beams in buildings and other structures.
N
V2
V1
T
M2
M1

## Slide 4: Shear and Moment Diagrams
In a horizontal beam:
  The shear diagram is used to show the internal shearing force.
  The moment diagram is used to show the internal bending moment
a
a

## Slide 5: Creating the Shear Diagram
Solve for all external forces and moments on the beam.
Draw a free body diagram of the horizontal beam, including all forces and moments
  Leave any distributed forces as distributed forces and do not replace with the equivalent point load.
Draw a set of axes below the free body diagram.
  The x axis will represent the location, lining up with the free body diagram above it.
  The y axis will represent the internal shearing force
To fill in the graph, start at the left at zero and as you move right…
  Each time you encounter a point force, jump that far up (for forces in the positive y direction) or down (for forces in the negative y direction)
  Each time you encounter a uniform distributed force, the shear diagram will be a line having the slope of the distributed force (same sign convention as before)
  Each time you encounter a non-uniform distributed force, the shear diagram will be the integral of the distributed force function (just as a line is the integral of a uniform constant distributed force)
  Ignore any moments in the diagram for now.

## Slide 6: Creating the Shear Diagram
3 m
3 m
3 m
7 m
6 kN
1 kN/m
36 kN m
Force (kN)
Location (m)
-6 kN
4.2 kN
7.8 kN
-1.8 kN
-4.8 kN
3 kN

## Slide 7
3 m
3 m
3 m
7 m
6 kN
1 kN/m
36 kN m
Force (kN)
Location (m)
-6 kN
4.2 kN
7.8 kN
-1.8 kN
-4.8 kN
3 kN

## Slide 8: Creating the Moment Diagram
You need to first draw the shear diagram.
Draw a set of axes lined up below the shear diagram.
  The x axis will represent the location, lining up with the shear diagram and free body diagram above it.
  The y axis will represent the internal bending moment.
To fill in the graph, start at the left at zero and as you move right…
  The moment diagram for the most part will be the integral of the shear diagram.
  If you encounter any moments directly applied to the beam, this will cause a jump in the moment diagrams
    Positive moments cause a downward jump in the moment diagram
    Negative moments cause an upward jump in the moment diagram

## Slide 9: Creating the Moment Diagram
Force (kN)
Location (m)
-6 kN
-1.8 kN
-4.8 kN
Shear Diagram
Moment (kNm)
Location (m)
-18 kNm
Moment Diagram
3 m
3 m
3 m
7 m
3 kN
18 kNm
5.4 kNm
-4.5 kNm

## Slide 10: Thanks for Watching
See other engineering mechanics videos and access the full tool at…

## Slide 11: Building the Moment Diagram Worked Example
Draw the moment diagram for the beam shown below.
3 m
3 m
3 m
7 m
6 kN
1 kN/m
36 kN m

## Slide 12: Complex Bending Practice Problem
A horizontal wooden beam in the lobby of a new hotel is going to be supported and loaded as shown below. What do the shear and moment diagram for this beam look like? What is the largest internal moment in the beam and where does it occur?
600 lbs
100 lbs/ft
100 lbs/ft
50 lbs/ft
3 ft
3 ft
3 ft
3 ft
4 ft